2009 CASPER Workshop
Tutorial 2: 10GbE Interface

Author:	Jason Manley and Andrew Martens

	Expected completion time: 2hrs

Contents:
    * Introduction

# Introduction
In this tutorial, you will create a simple Simulink design which uses the ROACH's 10GbE ports to send data at high speeds to another port. This could just as easily be another ROACH board or a computer with a 10GbE network interface card. In addition, we will learn to control the design remotely, using a supplied Python library for KATCP.

# Background
Roach boards have four CX-4 ports. There are two 156.25MHz crystals on the board. Each one clocks two ports, 0 & 1 and 2 & 3. This clock is then multiplied up on the FPGA by a factor of 20. Each port port has 4 channels running in parallel (hence the digit in CX-4). Thus, the speed on the wire is actually 4 x 156.25MHz x 20 = 12.5Gbps.

However, 10GbE uses 8/10 encoding, which means that for every byte sent, 10 bits are actually transmitted. This is to ensure proper clocking, since the receiver recovers and locks-on to the transmitter's clock and requires edges in the data. Imagine transmitting a string of 0xFF or 0b11111111... which would otherwise generate a DC level on the line, now an extra two bits are introduced which includes a zero bit which the receiver can use to recover the clock and byte endings. See http://en.wikipedia.org/wiki/8b/10b_encoding for more information.

For this reason, we actually get 12.5Gbps * 8/10 = 10Gbps usable datarate.

CASPER's 10GbE Simulink core sends and receives UDP over IPv4 packets, over Ethernet frames.

Each ethernet frame requires a 38 bytes, with a minimum payload size of 46 and a maximum usable payload of 1500 bytes. On top of this, IPv4 requires another 20 bytes and UDP a further 16. So for each packet of data you send, you will incur a cost of at least 74 bytes. I say at least, because the core will zero-pad some headers to be on a 64-bit boundary. You will thus never achieve 10Gbps of usable throughput. The best I have managed without loss is ~9.5Gbps. It pays to send larger packets if you are trying to get higher throughputs.

The maximum payload length of the CASPER 10GbE_v2 core is 8192 bytes (implemented in BRAM) plus another 512 (implemented in distributed RAM) which is useful for an application header.

These ports (and hence part of the10 GbE cores) run at 156.25MHz, while the interface to your design runs at the FPGA clock rate (sys_clk, adcX_clk etc). The interface is asynchronous, and buffers are required at the clock boundary. For this reason, even if you send data between two ROACH boards which are running off the same hard-wired clock, there will be jitter in the data.

A second consideration is how often you clock values into the core when you try to send data. If your FPGA is running faster than the core, and you try'n clock data in on every clock cycle, the buffers will eventually overflow. Likewise for receiving, if you send too much data to a board and cannot clock it out of the receive buffer fast enough, they will overflow and you will lose data.

In our design, we are clocking the FPGA at 200MHz, with the cores running at 156.25MHz. We will thus not be able to clock data into the TX buffer continuously for very long before it overflows. If this doesn't make much sense to you now, don't worry, it will become clear after you've tried it.

<<<< DIAGRAMS OF BUFFERS illustrating different input/output rates would ease readability>>>>

# Setup
The lab at the workshop is preconfigured with the CASPER libraries, Matlab and Xilinx tools. Simply double-click the mlib_devel_10_1 icon on the desktop to start Matlab with all required libraries.

# Creating Your Design
## Create a new model:
Start Matlab and open Simulink (either by typing simulink on the Matlab command line, or by click in the Simulink icon in the taskbar). Create a new model and add the Xilinx System Generator and XSG core config blocks as before in Tutorial 1.

Specify sys_clk_2x as the clock source.

Discuss concept of subsystems

discuss use of scopes

explain signalflows into/out of 10gbe core. Explain that we can't clock data in on every clock cycle indefinitely since fpga clk@200mhz, but cores only at 156.25MHz.

Discuss use of snap block, 64 bit versions and need for custom snapshot blocks for TX and RX. Also reason for t0 going to MSB, with t3 going to LSB because readout from PPC is most-sig first.

Explain that ROACH's LEDs are inverted.

recap katcp concepts from tut1

discuss need to set MAC addresses and numbering scheme (02:xx:xx:xx:xx:xx is private)

<compile time is 1hr 05 minutes. PROVIDE PRECOMPILED binary>