2010 CASPER Workshop
Tutorial 4: Narrowband Poco

Author:	Jason Manley

	Expected completion time: 2hrs

Contents:
    * Introduction

# Introduction
In this tutorial, you will create a simple Simulink design which uses the iADC board on ROACH and the CASPER DSP blockset to process a wideband signal, channelise it and output the spectrum through ROACH's PPC.

By this stage, we expect you have completed tutorials 1 and 2 and are reasonably comfortable with Simulink and basic Python. We will focus here on higher-level design concepts, and will provide you with low-level detail pre-implemented.

# Setup
The lab at the workshop is preconfigured with the CASPER libraries, Matlab and Xilinx tools. Simply double-click the mlib_devel_10_1 icon on the desktop to start Matlab with all required libraries.

# Background

# Creating Your Design
## Create a new model:
Start Matlab and open Simulink (either by typing simulink on the Matlab command line, or by click in the Simulink icon in the taskbar). Create a new model and add the Xilinx System Generator and XSG core config blocks as before in Tutorial 1.

<explain adc input demux by 4>
<demonstrate with scopes and simulink-domain mux-by-four>

<explain different versions of PFB and FFT>
<explain use of downshift by one bit to prevent overflows at first fft stage>

<explain need for sync inputs to demarkate first channel and make sense of FFT output>
<explain minimum sync period, why this can't be FFT_length and decision for 2^27 which doubles as heartbeat LED>

CONTROL:

design starts by itself. Only control register is for resetting counters.

Sync LED provides a “heartbeat” signal to instantly see if your design is clocked sensibly.

New accumulation LED gives a visual indication of datarates and dumptimes.

Accumulation counter provides simple mechanism for checking if a new spectrum output is available. (poll and compare to last value)